## Slide 1
Image Enhancement using Zero Memory Point Operations
Kiran TALELE
 99 870 30 881

## Slide 2
@ Bharatiya Vidya Bhavans’ Sardar Patel Institute of Technology Andheri(w) Mumbai
Associate Professor, Electronics Engineering Department (1997)
Dean, Students, Alumni & External Relations (2022)
@ Sardar Patel Technology Business Incubator(SP-TBI),
Funded by Department of Science & Technology(DST),
Govt. of India
Head, Academic Relations (2015)
@ IEEE Bombay Section
Treasurer (2020)
Executive Committee Member (2015)
Kiran TALELE
Kiran TALELE
2

## Slide 3: Objective :
IMP : The enhancement process does not increase the inherent information content in the data.
But it does increase the dynamic range of the chosen feature so that they con be detected easily.
Image Enhancement
To process a given image so that the result is more suitable than the original image for a specific application.
Kiran TALELE 99870 30 881 talelesir@gmail.com
3

## Slide 4
    Let r denotes input image pixel value
and s denotes output image pixel value
Then S = T (r)
where T is any Spatial Domain Tx function.
[1] Image Enhancement using Zero Memory Point Operations
Kiran TALELE 99870 30 881 talelesir@gmail.com
4

## Slide 5: Basic Gray Level Transformations using Zero Memory Point Operations
Contrast Stretching Transformations
Clipping and Thresholding
Digital Negative
LOG Transformation
Power Law Transformation
Intensity Level Slicing
Bit Level slicing
Kiran TALELE 99870 30 881 talelesir@gmail.com
5

## Slide 6: [1] Contrast Stretching Transformaton
(i) Low Contrast Image occur often due to
Poor or Non-uniform Lighting conditions
Limited dynamic range of imaging sensor
Improper setting of lens aperature.
Kiran TALELE 99870 30 881 talelesir@gmail.com
6

## Slide 7
A Contrast Stretching Transformation function can be achieved by
Stretching Dark range of input values into wider range of output values.
Shifting Mid range of input values
Compressing Bright range of input values.
s
r
0 a b (L-1)
(L-1)
S2
S1
0
7
Dark range
Mid range
Bright range

## Slide 8
where T is Contrast Stretching Tx function such that,
(iii) Mathematically,
It is defined as S= T(r)
S
r
0 a b (L-1)
(L-1)
S2
S1
0
Input Image
Output Image

## Slide 9
Ex. Obtain the gray level transformation function that :
Stretches gray scale range [0, 10] into [0, 15]
Shifts the range [10,20] to [15,25] and
Compresses the range [20,30] into [25,30].
Kiran TALELE 99870 30 881 talelesir@gmail.com
9

## Slide 10
ANS : Gray level transformation function that :
Stretches gray scale range
[0, 10] into [0, 15]
0 10
15
0
25
20
30
30
Shifts the range
[10,20] to [15,25] and
Compresses the range
[20,30] into [25,30].
s
r
0 a b (L-1)
(L-1)
S2
S1
0
Kiran TALELE 99870 30 881 talelesir@gmail.com
10
α
β
γ
α = 1.5 β = 1.0 γ = 0.5

## Slide 11
Kiran TALELE 99870 30 881 talelesir@gmail.com
A Contrast Stretching Tx function is given by,
Where a = 10 b = 20
L-1 = 30
S1 = 15 S2 = 25
α = 1.5 β = 1.0 γ = 0.5
11
1.5 r
S = r + 5
S = 10 + (0.5) (r-b )
By substituting we get,

## Slide 12
s
r
0 a b (L-1)
(L-1)
S2
S1
0
Q1. Derive Contrast Stretching
Transformation Function.
Case-1 : When 0<= r <= a
To find Slope
α =
(ii) To find Slope
α =
S = α r - - - - - (I)
(r,s)

## Slide 13
s
r
0 a b (L-1)
(L-1)
S2
S1
0
Case-2 : When a < r < = b
To find Slope
β =
(ii) To find Slope
β =
(r,s)
(a,s1)
(b,s2)
S - S1 = β (r-a)
S = S1 + β (r-a) - - - -(II)
Kiran TALELE 99870 30 881 talelesir@gmail.com
13

## Slide 14
s
r
0 a b (L-1)
Case-3 : When b < r < =(L-1)
To find Slope
ϒ =
(ii) To find Slope
ϒ =
(r,s)
(L-1)
S2
S1
0
(b,s2)
(L-1, L-1)
S - S2 = ϒ (r-b)
S = S2 + ϒ (r-b) - - - (III)
Kiran TALELE 99870 30 881 talelesir@gmail.com
14

## Slide 15
From equation (I), (II) and (III) we get,
α r
S = S1 + β (r-a)
S = S2 + ϒ (r-b )
Kiran TALELE 99870 30 881 talelesir@gmail.com
15
r
0 a b (L-1)
(L-1)
S2
S1
0
α
β
γ
s

## Slide 16
Q2. Apply following Transformation function on the image F and obtain new image.
r
0 4 8 15
15
12
8
0
S
Kiran TALELE 99870 30 881 talelesir@gmail.com
16

## Slide 17
A Contrast Stretching Tx function is given by,
r
Where
a = 4 b = 8
L-1 = 30
S1 = 8 S2 = 12
α = 2 β = 1 γ = 3/7
Kiran TALELE 99870 30 881 talelesir@gmail.com
17
0 4 8 15
15
12
8
0
S
α
β
γ

## Slide 18
By substituting we get,
Output image A is then given by,
A =
Kiran TALELE 99870 30 881 talelesir@gmail.com
18
11 |  |  |  | 
2 r
r + 4
12 + 0.43 (r – 8)

## Slide 19
By substituting we get,
Output image A is then given by,
11 | 14 | 4 | 6 | 8
A =
Kiran TALELE 99870 30 881 talelesir@gmail.com
19
2 r
r + 4
12 + 0.43 (r – 8)

## Slide 20
By substituting we get,
Output image A is then given by,
11 | 14 | 4 | 6 | 8
13 | 15 | 2 | 10 | 11
14 | 8 | 12 | 15 | 14
12 | 1 | 4 | 15 | 4
13 | 14 | 6 | 6 | 9
A =
Kiran TALELE 99870 30 881 talelesir@gmail.com
20
2 r
r + 4
12 + 0.43 (r – 8)

## Slide 21
A =
Kiran TALELE 99870 30 881 talelesir@gmail.com
21

## Slide 22
22
Kiran TALELE 99870 30 881 talelesir@gmail.com

## Slide 26: [2] Clipping and Thresholding
(ii) A Contrast Stretching Tx function is given by,
It is a special case of Contrast Stretching
Tx function.
Kiran TALELE 99870 30 881 talelesir@gmail.com
26

## Slide 27: Clipping . . .
Case-1 : When α = 0 and γ = 0
0 a b (L-1)
(L-1)
S2
S1
0
S
r
Case-2 : When α = 0, γ = 0 and S1= 0
0 = a b (L-1)
(L-1)
S2
S1=0
S
r

## Slide 28: Thresholding . . .
Case-3 : When α = 0, γ = 0, S1= 0 and a == b
0 a=b (L-1)
S2
0
S
r
0 T (L-1)
(L-1)
S
r
Thresholding Simplifies
Kiran TALELE 99870 30 881 talelesir@gmail.com

## Slide 29: Q4 Given Image F and Transformation Function. (a) Obtain the new image. (b) Plot Histogram of input & output Image (c) Compare the histograms of I/O image.
S
2
0,0
6
r
8
Kiran TALELE 99870 30 881 talelesir@gmail.com
29
2 | 3 | 4 | 2
5 | 5 | 2 | 4
3 | 6 | 3 | 5
5 | 3 | 5 | 5
F =

## Slide 30: (a) Obtain the new image Solution : To obtain New Image
S
(2,0)
0,0
r
8
Case-1 : When 0<= r <= 2
S = 0 ----(I)
Case-2 : When 2< r <= 6
To find Slope
β =
(ii) To find Slope
β =
(r,s)
(6,8)
S = 2 ( r - 2 ) - - - -(II)
= 2
= 2

## Slide 31
Case-3 : When r > 6
S = 8 ----(III)
From equation (I), (II) and (III) we get,
0
S = 8
S = 2 ( r - 2 )
0<= r <= 2
2< r <= 6
r > 6
S
2
0,0
6
r
8
Kiran TALELE 99870 30 881 talelesir@gmail.com
31

## Slide 32
0
S = 8
S = 2 ( r - 2 )
0<= r <= 2
2< r <= 6
r > 6
Output image A is then given by, A = T{ r}
0 |  |  | 0
 |  | 0 | 
A =
2 | 3 | 4 | 2
5 | 5 | 2 | 4
3 | 6 | 3 | 5
5 | 3 | 5 | 5
F =
Kiran TALELE 99870 30 881 talelesir@gmail.com
32

## Slide 33
0
S = 8
S = 2 ( r - 2 )
0<= r <= 2
2< r <= 6
r > 6
Output image A is then given by, A = T{ r}
A =
2 | 3 | 4 | 2
5 | 5 | 2 | 4
3 | 6 | 3 | 5
5 | 3 | 5 | 5
F =
0 | 2 | 4 | 0
6 | 6 | 0 | 4
2 |  | 2 | 6
6 | 2 | 6 | 6
Kiran TALELE 99870 30 881 talelesir@gmail.com
33

## Slide 34
0
S = 8
S = 2 ( r - 2 )
0<= r <= 2
2< r <= 6
r > 6
Output image A is then given by, A = T{ r}
A =
2 | 3 | 4 | 2
5 | 5 | 2 | 4
3 | 6 | 3 | 5
5 | 3 | 5 | 5
F =
0 | 2 | 4 | 0
6 | 6 | 0 | 4
2 | 6 | 2 | 6
6 | 2 | 6 | 6
Kiran TALELE 99870 30 881 talelesir@gmail.com
34

## Slide 35: (b) To plot Histogram
A =
2 | 3 | 4 | 2
5 | 5 | 2 | 4
3 | 6 | 3 | 5
5 | 3 | 5 | 5
F =
0 | 2 | 4 | 0
6 | 6 | 0 | 4
2 | 8 | 2 | 6
6 | 2 | 6 | 6
Input Image :
Ouput Image :
Kiran TALELE 99870 30 881 talelesir@gmail.com
35

## Slide 36
36
Input Image :
0 | 2 | 4 | 0
6 | 6 | 0 | 4
2 | 8 | 2 | 6
6 | 2 | 6 | 6
Frequency Table of input image :
Gray Value | Frequency
0 | 0
1 | 0
2 | 3
3 | 4
4 | 2
5 | 6
6 | 1
7 | 0
8 | 0
F =
Histogram of Input Image :
2 | 3 | 4 | 2
5 | 5 | 2 | 4
3 | 6 | 3 | 5
5 | 3 | 5 | 5
Freq
0 1 2 3 4 5 6 7 8 r
3
4
2
6
1

## Slide 37
37
Output Image :
0 | 2 | 4 | 0
6 | 6 | 0 | 4
2 | 8 | 2 | 6
6 | 2 | 6 | 6
Frequency Table of Output image :
Gray Value | Frequency
0 | 3
1 | 0
2 | 4
3 | 0
4 | 2
5 | 0
6 | 6
7 | 0
8 | 1
A =
Histogram of Output Image :
0 | 2 | 4 | 0
6 | 6 | 0 | 4
2 | 8 | 2 | 6
6 | 2 | 6 | 6
Freq
0 1 2 3 4 5 6 7 8 S
4
2
6
1
3

## Slide 38: (c) Compare of Input and Output image Histogram
Input Image has limited pixel range [2-6].
So, input image has LOW contrast.
Input Image pixel range [2-6] is increased to
[0-8] in the output image.
Thus, Contrast of output image is improved.
3. Distribution of pixels is NOT uniform in both input and output image,
Kiran TALELE 99870 30 881 talelesir@gmail.com
38

## Slide 39
0 1 2 3 4 5 6 7 8
Freq
0 1 2 3 4 5 6 7 8
3
4
2
6
1
r
Histogram of Input Image :
Histogram of Output Image :
Freq
4
2
6
1
3
S
Input Image has limited pixel range [2-6].
Thus, input image has LOW Contrast
Input Image pixel range [2-6] is increased to
[0-8] in the output image.
Thus, Contrast of output image is improved.

## Slide 40
Histogram of Input Image :
Freq
0 1 2 3 4 5 6 7 8
3
4
2
6
1
r
Histogram of Output Image :
Freq
0 1 2 3 4 5 6 7 8
4
2
6
1
3
S
3. Distribution of pixels is NOT uniform in both input and output image

## Slide 41
Kiran TALELE 99870 30 881 talelesir@gmail.com
Ex. Given Threshold T = 4
A =
0 | 0 | 0 | 0
0 | 0 | 15 | 15
15 | 0 | 0 | 0
0 | 0 | 15 | 15
Ouput Image :
Solution :
By Thresholding Tx,
If r > (T = 4)
Then
S = 15 (Max = L-1)
Else
S = 0
Max Pixel Value = 8
So, L = 24 == 16

## Slide 42
Q5 Convert the gray image to Binary Image.
Select appropriate value of threshold from
the histogram.
Kiran TALELE 99870 30 881 talelesir@gmail.com
42

## Slide 43
Kiran TALELE 99870 30 881 talelesir@gmail.com
43
Kiran TALELE 99870 30 881 talelesir@gmail.com
43
Frequency Table of image F:
Gry Value | Frequency
0 | 
1 | 
2 | 
3 | 
4 | 
5 | 
6 | 
7 | 
Solution : To plot Histogram of Input Image :

## Slide 44
Kiran TALELE 99870 30 881 talelesir@gmail.com
44
Kiran TALELE 99870 30 881 talelesir@gmail.com
44
Frequency Table of image F:
Gray Value | Frequency
0 | 5
1 | 3
2 | 2
3 | 1
4 | 2
5 | 3
6 | 4
7 | 5
Solution : To plot Histogram of Input Image :

## Slide 45
Kiran TALELE 99870 30 881 talelesir@gmail.com
45
Kiran TALELE 99870 30 881 talelesir@gmail.com
45
Frequency Table of image F:
Gray Value | Frequency
0 | 5
1 | 3
2 | 2
3 | 1
4 | 2
5 | 3
6 | 4
7 | 5
Histogram of Input Image :
Freq
0 1 2 3 4 5 6 7
2
1
2
3
1
r
3
4
5
5

## Slide 46
Kiran TALELE 99870 30 881 talelesir@gmail.com
46
Kiran TALELE 99870 30 881 talelesir@gmail.com
46
Let Threshold Value T = 3
Output Image :
A =
If r > (T = 3)
Then
S = 7
Else
S = 0
Input Image :
Let S = T ( r )
Where r is the input image pixel value and S is the output image pixel value

## Slide 47
Kiran TALELE 99870 30 881 talelesir@gmail.com
47
Kiran TALELE 99870 30 881 talelesir@gmail.com
47
Let Threshold Value T = 3
Let S = T ( r )
Where r is the input image pixel value and S is the output image pixel value
Output Image :
A =
0 | 0 | 0 | 0 | 0
0 | 7 | 7 | 7 | 0
0 | 7 | 7 | 7 | 7
7 | 7 | 0 | 0 | 0
7 | 7 | 7 | 7 | 7
If r > (T = 3)
Then
S = 7
Else
S = 0
Input Image :

## Slide 48: Example of Thresholding Transformation
Original
image
T=128
T=200
T=50
Histogram

## Slide 49: [3] Digital Negative
49
Negative Image is obtained by reverse scaling of gray levels of input image.
(i) Mathematically
S = (L-1) - r
0
r
s
(L-1)
0
(L-1)
(ii) Graphically
To find Slope
α =
To find Slope
α =
( r, s )
= -1
= -1
S = α[ r - (L-1) ]

## Slide 50
Application :
[2] To display Medical Images
[1] To obtain negative prints of Photograph
Kiran TALELE 99870 30 881 talelesir@gmail.com
50

## Slide 51
Kiran TALELE 99870 30 881 talelesir@gmail.com
Ex. Given Obtain Negative Image
A =
11 | 13 | 12 | 15
14 | 12 | 10 | 7
10 | 12 | 13 | 14
13 | 11 | 9 | 8
Ouput Image :
To find Output Image A:
By Digital Nagative Tx,
S = 15 - r
Where L = 24 == 16
S = (L-1) - r

## Slide 52: [4] LOG Transformation
(i) Mathematically,
Kiran TALELE 99870 30 881 talelesir@gmail.com
52
S = C Log ( 1 + r )
Where,
r is input image pixel value
S is output image pixel value
And C is any Constant
Application :
To display Fourier Transformed Image

## Slide 53: (ii) Graphically,
LOG Tx, Enhances small magnitude input values into wider range of output values
(ii) LOG Tx, Compresses large magnitude input values into narrow range of output values
Kiran TALELE 99870 30 881 talelesir@gmail.com
53
0
r
s
(L-1)
0
(L-1)

## Slide 54: Q6 Given Image F, Obtain the new image using LOG Transformation.
Kiran TALELE 99870 30 881 talelesir@gmail.com
54
128 | 212 | 25
54 | 0 | 124
4 | 152 | 15
F =

## Slide 55: Sol : Let S = T(r)
Kiran TALELE 99870 30 881 talelesir@gmail.com
55
128 | 212 | 25
54 | 0 | 124
4 | 152 | 15
F =
S = C Log ( 1 + r )
Assume C =1
Then S = Log10 ( 1 + r )
For F(0,0) =128 Find A(0,0)
A(0,0) = Log10 ( 1 + 128)
2 | 2 | 1
2 | 0 | 2
1 | 2 | 1
A =
A(0,0) = 2.11
Let A(0,0) == 2
Input Image
Output Image

## Slide 56: [5] Power Law Transformation
Mathematically,
Kiran TALELE 99870 30 881 talelesir@gmail.com
56
s = rγ
Where,
r is Normalized input image pixel value
S is Normalized output image pixel value

## Slide 57
When γ < 1
PLT maps narrow range of dark input values into wider range of ouput values
(ii) When γ = 1
Output Pixel Value = Input Pixel Value
(iii) When γ > 1
PLT maps wider range of input values into narrow range of ouput dark pixel values
0 1
1
0
S
r
γ =0.5
0 1
S
r
0 1
S
r
γ = 1
1
0
γ = 2
1
0

## Slide 58: Q6. For the image given below perform the operation S = r2
Kiran TALELE 99870 30 881 talelesir@gmail.com
58
A =
0 | 2 | 4 | 0
6 | 6 | 0 | 4
2 | 8 | 2 | 8
6 | 2 | 6 | 8

## Slide 59: Step-1 : Find Normalized Input Pixel values
Kiran TALELE 99870 30 881 talelesir@gmail.com
59
0 | 0.25 | 0.5 | 0
0.75 | 0.75 | 0 | 0.5
0.25 | 1 | 0.25 | 1
0.75 | 0.25 | 0.75 | 1
B =
A =
0 | 2 | 4 | 0
6 | 6 | 0 | 4
2 | 8 | 2 | 8
6 | 2 | 6 | 8
Input Image
Max Value = 8

## Slide 60: Step-1 : Find Normalized Input Pixel values
Kiran TALELE 99870 30 881 talelesir@gmail.com
60
0 | 0.25 | 0.5 | 0
0.75 | 0.75 | 0 | 0.5
0.25 | 1 | 0.25 | 1
0.75 | 0.25 | 0.75 | 1
Step-2 : Apply Power
Law Transformation
S = r2
0 | 0.0625 | 0.25 | 0
0.5625 | 0.5625 | 0 | 0.25
0.0625 | 1 | 0.0625 | 1
0.5625 | 0.0625 | 0.5625 | 1
B =
C =

## Slide 61: Step-3 : Find De-normalized output Pixel values
De-normalized = Power Law Tx MAX Input value Output value Value
Kiran TALELE 99870 30 881 talelesir@gmail.com
61
0 | 0.5 | 2 | 0
4.5 | 4.5 | 0 | 2
0.5 | 8 | 0.5 | 8
4.5 | 0.5 | 4.5 | 8
0 | 1 | 2 | 0
5 | 5 | 0 | 2
1 | 8 | 1 | 8
5 | 1 | 5 | 8
=
=
0 | 0.0625 | 0.25 | 0
0.5625 | 0.5625 | 0 | 0.25
0.0625 | 1 | 0.0625 | 1
0.5625 | 0.0625 | 0.5625 | 1
= (8)

## Slide 62: Application : Gamma Correction
Kiran TALELE 99870 30 881 talelesir@gmail.com
62
A cathode ray tube (CRT), converts a video signal to light in a nonlinear way. The light intensity is proportional to a power (γ) of the source voltage
For a computer CRT, γ is about 2.2
Viewing images properly on monitors requires γ-correction

## Slide 63: Gamma Correction

## Slide 64: Image Enhancement by PLT
Aerial Image
PLT output
images with
(b) γ = 3.0
γ = 4.0 and
γ = 5.0
Input Image (a)
(…Courtesy of NASA)
a | b
d | c

## Slide 65: [6] Intensity Level Slicing
Highlighting a specific range of input values is called Intensity Level Slicing
Kiran TALELE 99870 30 881 talelesir@gmail.com
65
Case-1 : Without Background
(Ii) Mathematically
(i) Graphically
0
r
s
(L-1)
0
(L-1)
a b
S = L-1 if a < r < b
= 0 Otherwise

## Slide 66
Kiran TALELE 99870 30 881 talelesir@gmail.com
66
Case-2 : With Background
(ii) Mathematically
(i) Graphically
S = L-1 if a < r < b
= r Otherwise
s
0
r
(L-1)
0
(L-1)
a b

## Slide 67: Q7. For the image given below perform the Intensity Level Slicing for a = 2 and b = 5 with background and without background
Kiran TALELE 99870 30 881 talelesir@gmail.com
67
A =
4 | 2 | 3 | 0
1 | 3 | 5 | 7
5 | 3 | 2 | 1
2 | 4 | 6 | 7

## Slide 68
Kiran TALELE 99870 30 881 talelesir@gmail.com
68
Kiran TALELE 99870 30 881 talelesir@gmail.com
68
Solution :
Output Image :
A =
7 | 0 | 7 | 0
Input Image :
Let S = T ( r )
Where r is the input image pixel value and S is the output image pixel value
Case-1 : Without Background
S = 7 if 2 < r < 5
i.e. {r = 3, 4}
= 0 Otherwise
F =
4 | 2 | 3 | 0
1 | 3 | 5 | 7
5 | 3 | 2 | 1
2 | 4 | 6 | 7

## Slide 69
Kiran TALELE 99870 30 881 talelesir@gmail.com
69
Kiran TALELE 99870 30 881 talelesir@gmail.com
69
Solution :
Output Image :
A =
7 | 0 | 7 | 0
0 | 7 | 0 | 0
0 | 7 | 0 | 0
0 | 7 | 0 | 0
Input Image :
Let S = T ( r )
Where r is the input image pixel value and S is the output image pixel value
Case-1 : Without Background
S = 7 if 2 < r < 5
i.e. {r = 3, 4}
= 0 Otherwise
F =
4 | 2 | 3 | 0
1 | 3 | 5 | 7
5 | 3 | 2 | 1
2 | 4 | 6 | 7

## Slide 70
Kiran TALELE 99870 30 881 talelesir@gmail.com
70
Kiran TALELE 99870 30 881 talelesir@gmail.com
70
Solution :
Output Image :
A =
7 | 2 | 7 | 0
1 | 7 | 5 | 7
5 | 7 | 2 | 1
2 | 7 | 6 | 7
Input Image :
Let S = T ( r )
Where r is the input image pixel value and S is the output image pixel value
Case-2 : With Background
S = 7 if 2 < r < 5
i.e. {r = 3, 4}
= r Otherwise
F =
4 | 2 | 3 | 0
1 | 3 | 5 | 7
5 | 3 | 2 | 1
2 | 4 | 6 | 7

## Slide 71
Highlight the major blood vessels and study the shape of the flow of the contrast medium (to detect blockages, etc.)
Measuring the actual flow of the contrast medium as a function of time in a series of images

## Slide 72: [7] Bit Level Slicing
Highlighting a specific bit of input pixel values is called Bit Level Slicing.
Kiran TALELE 99870 30 881 talelesir@gmail.com
72
Mathematically :
For r = [ bn,…b2, b1, b0 ]
If ( bn = 1 )
Then S = L-1
Otherwise S = 0

## Slide 73: Ex. Consider 3 bit image with r = [b2, b1, b0 ] and L-1 = 7
Kiran TALELE 99870 30 881 talelesir@gmail.com
73
A =
0 | 2 | 4
3 | 6 | 3
5 | 7 | 1
=
To highlight MSB bit of every pixel :
000 | 010 | 100
011 | 110 | 011
101 | 111 | 001
For r = [ b2, b1, b0 ]
If ( b2 = 1 )
Then S = 7
Otherwise S = 0
B =
0 | 0 | 7
0 | 7 | 0
7 | 7 | 0

## Slide 74: Dr. Kiran TALELE
091-9987030881
kiran.talele@spit.ac.in / ktvtalele@gmail.com
74
74
Academic : PhD
Professional :
  Dean-Students, Alumni & External Relations @ Bharatiya Vidya Bhavans’ Sardar Patel Institute of Technology (SP-IT), Mumbai
  Head-Academic Relation @ Sardar Patel Technology Business Incubator (SP-TBI), Mumbai
  Treasurer-IEEE Bombay Section
https://www.linkedin.com/in/k-t-v-talele/
www.facebook.com/Kiran-Talele-1711929555720263
Stay Connected

## Slide 75
Dr. Kiran TALELE is an Associate Professor in Electronics & Telecommunication Engineering Department of Bharatiya Vidya Bhavans’ Sardar Patel Institute of Technology, Mumbai with 33+ years experience in Academics.
He is a Dean of Students, Alumni and External Relations at Sardar Patel Institute of Technology, Andheri Mumbai.
He is also a Head of Sardar Patel Technology Business Incubator, Mumbai.
His area of research is Digital Signal & Image Processing, Computer Vision, Machine Learning and Multimedia System Design.
He has published 85+ research papers at various national & international refereed conferences and journals. He has filed published 25+ patents at Indian Patent Office. One patent is granted in 2021.
He is a Treasurer of IEEE Bombay Section and Mentor for Startup Incubation & Intellectual Asset Creation.
He is a recipient of P.R. Bapat IEEE Bombay Section Outstanding Volunteer Award 2019.

## Slide 76
Kiran TALELE 99870 30 881 talelesir@gmail.com
76