## Slide 1
Image Enhancement Using Spatial Filtering
Kiran TALELE
 99 870 30 881

## Slide 2
@ Bharatiya Vidya Bhavans’ Sardar Patel Institute of Technology Andheri(w) Mumbai
Associate Professor, Electronics Engineering Department (1997)
Dean, Students, Alumni & External Relations (2022)
@ Sardar Patel Technology Business Incubator(SP-TBI),
Funded by Department of Science & Technology(DST),
Govt. of India
Head, Academic Relations (2015)
@ IEEE Bombay Section
Treasurer (2020)
Executive Committee Member (2015)
Kiran TALELE
Kiran TALELE
2

## Slide 3
(i) In Neighbourhood opération, Tx. function works on a group of input pixel values
(ii) The Output pixel value at (x,y) position is obtained by masking operation
(iii) The use of spatial mask for image processing is called spatial filtering and the mask is called spatial filter
Image Enhancement by Neighbourhood Processing : Spatial Filtering
Kiran TALELE
3

## Slide 4
Masking Operation: Consider an image F and filter mask W
Z1 | Z2 | Z3
Z4 | Z5 | Z6
Z7 | Z8 | Z9
The response of mask is given by,
R = z1 w1 + z2 w2 + z3 w3 + … + z9 w9
 | R | 
Kiran TALELE
4
*
F=
A =

## Slide 5: Spatial Filtering
y
x
Input Image F
y
x
Output Image A
Spatial filter
F
A
O
1
2
3
4
5
6
7
8
9
O 1 2 3 4 5 6 7 8 9 10 11
O 1 2 3 4 5 6 7 8 9 10 11
O
1
2
3
4
5
6
7
8
9
Simple 3*3 Neighbourhood

## Slide 6: Spatial Filtering
w1
w2
w3
w4
w5
w6
w7
w8
w9
y
x
Input Image F
Filter Mask
z1
z2
z3
z4
z5
z6
z7
z8
z9
Original Image Pixels
*
The above is repeated for every pixel in the original image to generate the smoothed image
A(8,11) = z1 w1 + z2 w2 +
z3 w3+ … + z9 w9
The response of Filter at A(8,11) position is given by,
O
1
2
3
4
5
6
7
8
O 1 2 3 4 5 6 7 8 9 10 11
F(8,11)

## Slide 7
[I] Smoothing Linear Filters (3)
Eg. Low Pass Averaging Filter, Weighted Average Filter, Trimmed Averaging Filter and Geometric Mean Filter
[II] Smoothing Non-Linear Filters (3)
Eg. Median, Max and Min Filter.
[III] Sharpening : First Order Derivative Filters (4)
Eg. Robert, Prewit, Sobel and Fri-Chen filter
[IV] Sharpening Second Order Derivative Filters (3)
Eg. Laplacian Filter, HPF and High Boost Filter
List of Spatial Filters
Kiran TALELE
7

## Slide 8: [ I ] Smoothing Linear Filters
(i) LPF attenuates High frequency Components and allows to pass LOW frequency components of the image.
(ii) LPF reduces the difference between neighbouring pixels by distributing its’ energy using averaging technique.
(1) Low Pass Averaging Filter
Kiran TALELE
8

## Slide 9
(iii) LPF removes sharp transitions in the image
Sharp transitions are due to :
(1) High frequency random Impulse Noise.
(2) High frequency Edges of an object.
Kiran TALELE
9
.
.
.

## Slide 10
Eg. Consider a Digital Image F with impulse noise
L P F
0 | 0 | 0
0 | 200 | 0
0 | 0 | 0
Kiran TALELE
10
(IV) LPF reduces the difference between the neighbouring pixels by distributing its energy in all directions by averaging techniques
(v) The net effect of LP filtering is Image Blurring

## Slide 11
L P F
0 | 0 | 0
0 |  | 0
0 | 0 | 0
 | 22 | 
Kiran TALELE
11
Eg. Digital Image with impulse noise
LPF reduces the difference between the neighbouring pixels by distributing its energy in all directions by averaging techniques
200
22 | 22 | 22
22 |  | 22
22 | 22 | 22

## Slide 12
L P F
0 | 1 | 2
7 | 255 | 3
6 | 5 | 4
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 2 | 0
0 | 7 | 255 | 3 | 0
0 | 6 | 5 | 4 | 0
0 | 0 | 0 | 0 | 0
L P F
Eg-1 : Digital Image with impulse noise
Case-1 : Assume virtual Rows and Columns with Zero pixel
Values

## Slide 13
L P F
0 | 1 | 2
7 | 255 | 3
6 | 5 | 4
Kiran TALELE
13
L P F
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 2 | 0
0 | 7 | 255 | 3 | 0
0 | 6 | 5 | 4 | 0
0 | 0 | 0 | 0 | 0
Eg-1 : Digital Image with impulse noise

## Slide 14
L P F
0 | 1 | 2
7 | 255 | 3
6 | 5 | 4
Kiran TALELE
14
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 2 | 0
0 | 7 | 255 | 3 | 0
0 | 6 | 5 | 4 | 0
0 | 0 | 0 | 0 | 0
L P F
31
Eg-1 : Digital Image with impulse noise

## Slide 15
L P F
0 | 1 | 2
7 | 255 | 3
6 | 5 | 4
Kiran TALELE
15
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 2 | 0
0 | 7 | 255 | 3 | 0
0 | 6 | 5 | 4 | 0
0 | 0 | 0 | 0 | 0
L P F
31
29
Eg-1 : Digital Image with impulse noise

## Slide 16
L P F
0 | 1 | 2
7 | 255 | 3
6 | 5 | 4
Kiran TALELE
16
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 2 | 0
0 | 7 | 255 | 3 | 0
0 | 6 | 5 | 4 | 0
0 | 0 | 0 | 0 | 0
L P F
31
29
30
Eg-1 : Digital Image with impulse noise

## Slide 17
L P F
0 | 1 | 2
7 | 255 | 3
6 | 5 | 4
Kiran TALELE
17
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 2 | 0
0 | 7 | 255 | 3 | 0
0 | 6 | 5 | 4 | 0
0 | 0 | 0 | 0 | 0
L P F
31
29
30
30
Eg-1 : Digital Image with impulse noise

## Slide 18
L P F
0 | 1 | 2
7 | 255 | 3
6 | 5 | 4
Kiran TALELE
18
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 2 | 0
0 | 7 | 255 | 3 | 0
0 | 6 | 5 | 4 | 0
0 | 0 | 0 | 0 | 0
L P F
31
29
30
30
30
Eg-1 : Digital Image with impulse noise

## Slide 19
L P F
0 | 1 | 2
7 | 255 | 3
6 | 5 | 4
Kiran TALELE
19
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 2 | 0
0 | 7 | 255 | 3 | 0
0 | 6 | 5 | 4 | 0
0 | 0 | 0 | 0 | 0
L P F
31
29
30
30
30
Eg-1 : Digital Image with impulse noise

## Slide 20
L P F
0 | 1 | 2
7 | 255 | 3
6 | 5 | 4
Kiran TALELE
20
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 2 | 0
0 | 7 | 255 | 3 | 0
0 | 6 | 5 | 4 | 0
0 | 0 | 0 | 0 | 0
L P F
31
29
30
30
30
30
Eg-1 : Digital Image with impulse noise

## Slide 21
L P F
0 | 1 | 2
7 | 255 | 3
6 | 5 | 4
Kiran TALELE
21
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 2 | 0
0 | 7 | 255 | 3 | 0
0 | 6 | 5 | 4 | 0
0 | 0 | 0 | 0 | 0
L P F
31
29
30
30
30
30
30
Eg-1 : Digital Image with impulse noise

## Slide 22
L P F
0 | 1 | 2
7 | 255 | 3
6 | 5 | 4
Kiran TALELE
22
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 2 | 0
0 | 7 | 255 | 3 | 0
0 | 6 | 5 | 4 | 0
0 | 0 | 0 | 0 | 0
L P F
31
29
30
30
30
30
33
30
Eg-1 : Digital Image with impulse noise

## Slide 23
L P F
0 | 1 | 2
7 | 255 | 3
6 | 5 | 4
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 2 | 0
0 | 7 | 255 | 3 | 0
0 | 6 | 5 | 4 | 0
0 | 0 | 0 | 0 | 0
L P F
 |  | 30
30 | 33 | 
31
29
30
30
30
30
Eg-1 : Digital Image with impulse noise

## Slide 24
L P F
0 | 1 | 2
7 | 255 | 3
6 | 5 | 4
Kiran TALELE
24
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 2 | 0
0 | 7 | 255 | 3 | 0
0 | 6 | 5 | 4 | 0
0 | 0 | 0 | 0 | 0
L P F
31
29
30
30
30
30
30
33
30
Eg-2 : Consider a Digital Image with impulse noise

## Slide 25
L P F
0 | 1 | 2
7 | 255 | 3
6 | 5 | 4
Kiran TALELE
25
31
29
30
30
30
30
30
33
30
All the pixel in the neighourhood of impulse noise have almost same value.
Thus high frequency impulse noise is completely suppressed in the output image.

## Slide 26
L P F
0 | 1 | 2
7 | 255 | 3
6 | 5 | 4
0 | 0 | 1 | 2 | 2
0 | 0 | 1 | 2 | 2
7 | 7 | 255 | 3 | 3
6 | 6 | 5 | 4 | 4
6 | 6 | 5 | 4 | 4
L P F
30 | 30 | 30
32 | 31 | 31
34 | 33 | 32
Digital Image with impulse noise
Case-2 : Assume Virtual Rows and Columns with repeated border pixel Values
30 | 30 | 30
32 | 31 | 31
34 | 33 | 32

## Slide 27
L P F
Kiran TALELE
27
Eg-2. Digital Image with High Frequency Edge
10 | 73 | 137 | 200
10 | 73 | 137 | 200
10 | 73 | 137 | 200
10 | 10 | 200 | 200
10 | 10 | 200 | 200
10 | 10 | 200 | 200
200 | 200
200 | 200
200 | 200
10 | 10 | 200 | 200
10 | 10 | 200 | 200
10 | 10 | 200 | 200
10 | 10 | 10 | 200 | 200 | 200
10 | 10 | 10 | 200 | 200 | 200
10 | 10 | 10 | 200 | 200 | 200
10 | 10 | 10 | 200 | 200 | 200
10 | 10 | 10 | 200 | 200 | 200
L P F
 | 10 | 73 | 137 | 200 | 
 | 10 | 73 | 137 | 200 | 
 | 10 | 73 | 137 | 200 | 
.

## Slide 28
Summary :
All the pixels in the output image have almost same value.
Averaging of gray values in the neighbourhood reduces the sharp transitions in the images.
Thus High frequency Impulse noise is completely suppressed. This is desirable effect.
However high frequency edges are blurred.
This is undesired effect.
Kiran TALELE
28

## Slide 29
Derivation of LPF Mask
L P F
Z1 | Z2 | Z3
Z4 | Z5 | Z6
Z7 | Z8 | Z9
w1 | w2 | w3
w4 | w5 | w6
w7 | w8 | w9
Kiran TALELE
29
Consider a Digital Image F and LPF Mask w as shown in figure below,
The response of LPF mask at (x,y) position is given by,
R = z1 w1 + z2 w2 + z3 w3 + … + z9 w9 ……(I)

## Slide 30
Consider a Digital Image F and LPF Mask w as shown in figure below,
L P F
Z1 | Z2 | Z3
Z4 | Z5 | Z6
Z7 | Z8 | Z9
 | R | 
The response of LPF mask at A(x,y) position is given by,
R = z1 w1 + z2 w2 + z3 w3 + … + z9 w9 ……(I)
Kiran TALELE
30

## Slide 31
L P F
Z1 | Z2 | Z3
Z4 | Z5 | Z6
Z7 | Z8 | Z9
 | R | 
By averaging output pixel value at (x,y) position is given by,
Kiran TALELE
31
R = ( z1 + z2 + z3 + … + z9 )
R = z1 z1 + z2 + + … + z9 ) …… (II)

## Slide 32
1 | 1 | 1
1 | 1 | 1
1 | 1 | 1
By equating equation (I) and (II) we get,
Kiran TALELE
32
R = z1 w1 + z2 w2 + z3 w3 + … + z9 w9 ……(I)
R = z1 z1 + z2 + + … + z9 …… (II)
w1= | w2= | w3=
w4= | w5= | w6=
w7= | w8= | W9 =
w =
w =

## Slide 33
(i) In this filter, output pixel value at each (x,y) position is obtained by averaging the weighted neighbouring pixel values.
(2) Low Pass Weighted Averaging Filters
(ii) The Weight (i.e. Scaling factor) depends on the position of the neighbouring pixel with reference to the center pixel.
Kiran TALELE
33

## Slide 34
Kiran TALELE
34
 | Pixel Position | Weight
1 | Center Pixel | 4
2 |  | 
3 |  | 
Z1 | Z2 | Z3
Z4 | Z5 | Z6
Z7 | Z8 | Z9

## Slide 35
Kiran TALELE
35
 | Pixel Position | Weight
1 | Center Pixel | 4
2 | 4 Directional Neighbour | 2
3 |  | 

## Slide 36
Kiran TALELE
36
 | Pixel Position | Weight
1 | Center Pixel | 4
2 | 4 Directional Neighbour | 2
3 | Diagonal Direction Neighbour | 1

## Slide 37
Consider a Digital Image F and filter mask w as shown in fig below,,
Weighted Average Filter
Z1 | Z2 | Z3
Z4 | Z5 | Z6
Z7 | Z8 | Z9
 | 4 | 
Kiran TALELE
37
F =
A =

## Slide 38
Consider a Digital Image F and filter mask w as shown in fig below,
Weighted Average Filter
Z1 | Z2 | Z3
Z4 | Z5 | Z6
Z7 | Z8 | Z9
 | 2 | 
2 | 4 | 2
 | 2 | 
Kiran TALELE
38
F =
A =

## Slide 39
Consider a Digital Image F and filter mask w as shown in fig below,
Weighted Average Filter
Z1 | Z2 | Z3
Z4 | Z5 | Z6
Z7 | Z8 | Z9
1 | 2 | 1
2 | 4 | 2
1 | 2 | 1
Kiran TALELE
39
F =
A =

## Slide 40
Consider a Digital Image F and filter mask w as shown in fig below,
Weighted Average Filter
Z1 | Z2 | Z3
Z4 | Z5 | Z6
Z7 | Z8 | Z9
1 | 2 | 1
2 | 4 | 2
1 | 2 | 1
Kiran TALELE
40
F =
A =

## Slide 41
Weighted Average Filter
Z1 | Z2 | Z3
Z4 | Z5 | Z6
Z7 | Z8 | Z9
 | R | 
1 | 2 | 1
2 | 4 | 2
1 | 2 | 1
Kiran TALELE
41
F =
A =
The response of mask at A(x,y) position is given by,
R = [( z1 + 2 z2 + z3 )+( 2z4 + 4 z5 + 2 z6 )+ ( z7 + 2 z8 + z9 ) ]

## Slide 42
Kiran TALELE
42
(3) Trimmed Averaging Filter
A non-linear smoothing filter.
This filter deals well with images containing spiky noise, but it is less effective at attenuating random noise

## Slide 43
Kiran TALELE
43
Trimmed Mean Filter ALGORITHM :
1. Place a window over element;
2. Pick up elements;
3. Order elements;
Discard elements at the beginning and at the end of the got
ordered set;
Take an average — sum up the remaining elements and
divide the sum by their number.
Since the filter applies a mean to the untrimmed data, it is not edge preserving

## Slide 44
Kiran TALELE
44
(4) Alpha (α)-Trimmed Averaging Filter
A non-linear smoothing filter.
For ex. Consider below window size
20 | 20 | 8
21 | 19 | 12
19 | 22 | 10
The ordered list is :
F = { 8, 10, 12, 19, 19, 20, 20, 21, 22}
F =
A =
 | A(x,y) | 

## Slide 45
Kiran TALELE
45
F = { 8, 10, 12, 19, 19, 20, 20, 21, 22}
For different values of α, the output is as follows:
Case-1 : When α = 0
Case-2 : When α = 1
To find A(x,y)
A(x,y) = 18.8
A(x,y) = 17.3
F = { 8, 10, 12, 19, 19, 20, 20, 21, 22}

## Slide 46
Kiran TALELE
46
A(x,y) = 19.0
Case-3 : When α = 2
A(x,y) = 18.0
F = { 8, 10, 12, 19, 19, 20, 20, 21, 22}
Case-4 : When α = 3
A(x,y) = 19.3
F = { 8, 10, 12, 19, 19, 20, 20, 21, 22}
Case-5 : When α = 4
F = { 8, 10, 12, 19, 19, 20, 20, 21, 22}

## Slide 47
Kiran TALELE
47
This filter is a combination of mean filter and median filter as you said.
This is an algorithmic approach that tries to combine properties of the mean filter with properties of the median filter.

## Slide 48
Kiran TALELE
48
(5) Geometric Mean Filter
The geometric mean filter is an image filtering process meant to smooth and reduce noise of an image.
It is based on the mathematic geometric mean.
  The output image G(x,y) of a geometric mean is given by

## Slide 49
Kiran TALELE
49
Eg. Consider a digital subimage F
5 | 16 | 22
6 | 3 | 18
12 | 3 | 15
F =
A =
 | A(x,y) | 
Geometric Mean Filter
A(x,y) = (5 * 16 * 22 * 6 * 3 * 18 * 12 * 3 * 15)^(1/9)
A(x,y) = 8.77
The output pixel value at A(x,y) position is given by,

## Slide 50: [II] Smoothing Non-Linear Filters [ also called as ordered statistic filters]
(i) Medial filter is a Non-Linear ordered statistic filter.
(ii) Output pixel value at (x,y) position is obtained by selecting the median of neighbourhood of input pixel value.
(1) Median Filter
Kiran TALELE
50

## Slide 51
(I) Arrange the pixels in the window either in Increasing order OR in Decreasing order.
Select the middle value
If number of pixels in the window are even,
Then find average of the middle two values.
* Median Filter ALGORITHM
(III) Replace the input pixel value by the selected median value in the output image.
Kiran TALELE
51

## Slide 52
Kiran TALELE
52
Eg. Consider a Digital Image F
41 | 200 | 60
52 | 45 | 72
10 | 58 | 81
F =
1. Arrange All the pixel values in asceding order
Median Filter
A =
 | A(x,y) | 
10 | 41 | 45 | 52 | 58 | 60 | 72 | 81 | 200
2. Select the middle value
A(x,y) = 58

## Slide 53
Kiran TALELE
53
Ex of Digital Image with Salt and Pepper Noise :
41 | 200 | 60
52 | 45 | 42
0 | 58 | 51
F =
Salt Noise Value = 200 (White)
Pepper Noise Value = 0 (Black)
Most of the pixels in the image are in the range
[ 40 to 60 ]
There are two extreme values in the image :
i.e. 200 (Salt Noise) and 0 (Pepper Noise)

## Slide 54
Median Filter
41 | 200 | 60
52 | 45 | 42
0 | 58 | 51
Kiran TALELE
54
F =
To remove noisy pixels, assume virtual rows and columns with repeated border pixel values
 | 41 | 200 | 60 | 
 | 52 | 45 | 42 | 
 | 0 | 58 | 51 | 
F =

## Slide 55
Median Filter
41 | 200 | 60
52 | 45 | 42
0 | 58 | 51
Kiran TALELE
55
F =
To remove noisy pixels, assume virtual rows and columns with repeated border pixel values
 | 41 | 200 | 60 | 
41 | 41 | 200 | 60 | 60
52 | 52 | 45 | 42 | 42
0 | 0 | 58 | 51 | 51
 | 0 | 58 | 51 | 
F =

## Slide 56
Median Filter
41 | 200 | 60
52 | 45 | 42
0 | 58 | 51
Kiran TALELE
56
F =
To remove noisy pixels, assume virtual rows and columns with repeated border pixel values
41 | 41 | 200 | 60 | 60
41 | 41 | 200 | 60 | 60
52 | 52 | 45 | 42 | 42
0 | 0 | 58 | 51 | 51
0 | 0 | 58 | 51 | 51
F =
A =
A =
Median Filter

## Slide 57
Median Filter
41 | 200 | 60
52 | 45 | 42
0 | 58 | 51
Kiran TALELE
57
F =
To remove noisy pixels, assume virtual rows and columns with repeated border pixel values
41 | 41 | 200 | 60 | 60
41 | 41 | 200 | 60 | 60
52 | 52 | 45 | 42 | 42
0 | 0 | 58 | 51 | 51
0 | 0 | 58 | 51 | 51
F =
A =
A =
Median Filter

## Slide 58
Median Filter
41 | 200 | 60
52 | 45 | 42
0 | 58 | 51
Kiran TALELE
58
F =
To remove noisy pixels, assume virtual rows and columns with repeated border pixel values
41 | 41 | 200 | 60 | 60
41 | 41 | 200 | 60 | 60
52 | 52 | 45 | 42 | 42
0 | 0 | 58 | 51 | 51
0 | 0 | 58 | 51 | 51
F =
A =
A =
Median Filter
51

## Slide 59
Median Filter
41 | 200 | 60
52 | 45 | 42
0 | 58 | 51
Kiran TALELE
59
F =
To remove noisy pixels, assume virtual rows and columns with repeated border pixel values
41 | 41 | 200 | 60 | 60
41 | 41 | 200 | 60 | 60
52 | 52 | 45 | 42 | 42
0 | 0 | 58 | 51 | 51
0 | 0 | 58 | 51 | 51
F =
A =
A =
Median Filter
45

## Slide 60
Median Filter
41 | 200 | 60
52 | 45 | 42
0 | 58 | 51
Kiran TALELE
60
F =
To remove noisy pixels, assume virtual rows and columns with repeated border pixel values
41 | 41 | 200 | 60 | 60
41 | 41 | 200 | 60 | 60
52 | 52 | 45 | 42 | 42
0 | 0 | 58 | 51 | 51
0 | 0 | 58 | 51 | 51
F =
A =
A =
Median Filter
45 |  | 
52

## Slide 61
Median Filter
41 | 200 | 60
52 | 45 | 42
0 | 58 | 51
Kiran TALELE
61
F =
To remove noisy pixels, assume virtual rows and columns with repeated border pixel values
41 | 41 | 200 | 60 | 60
41 | 41 | 200 | 60 | 60
52 | 52 | 45 | 42 | 42
0 | 0 | 58 | 51 | 51
0 | 0 | 58 | 51 | 51
F =
A =
A =
Median Filter
45 | 52 | 
60

## Slide 62
Median Filter
41 | 200 | 60
52 | 45 | 42
0 | 58 | 51
Kiran TALELE
62
F =
To remove noisy pixels, assume virtual rows and columns with repeated border pixel values
41 | 41 | 200 | 60 | 60
41 | 41 | 200 | 60 | 60
52 | 52 | 45 | 42 | 42
0 | 0 | 58 | 51 | 51
0 | 0 | 58 | 51 | 51
F =
A =
A =
Median Filter
45 | 52 | 60
45

## Slide 63
Median Filter
41 | 200 | 60
52 | 45 | 42
0 | 58 | 51
Kiran TALELE
63
F =
To remove noisy pixels, assume virtual rows and columns with repeated border pixel values
41 | 41 | 200 | 60 | 60
41 | 41 | 200 | 60 | 60
52 | 52 | 45 | 42 | 42
0 | 0 | 58 | 51 | 51
0 | 0 | 58 | 51 | 51
F =
A =
A =
Median Filter
45 | 52 | 60
45 |  | 
51

## Slide 64
Median Filter
41 | 200 | 60
52 | 45 | 42
0 | 58 | 51
Kiran TALELE
64
F =
To remove noisy pixels, assume virtual rows and columns with repeated border pixel values
41 | 41 | 200 | 60 | 60
41 | 41 | 200 | 60 | 60
52 | 52 | 45 | 42 | 42
0 | 0 | 58 | 51 | 51
0 | 0 | 58 | 51 | 51
F =
A =
A =
Median Filter
45 | 52 | 60
45 | 51 | 
51

## Slide 65
Median Filter
41 | 200 | 60
52 | 45 | 42
0 | 58 | 51
Kiran TALELE
65
F =
To remove noisy pixels, assume virtual rows and columns with repeated border pixel values
41 | 41 | 200 | 60 | 60
41 | 41 | 200 | 60 | 60
52 | 52 | 45 | 42 | 42
0 | 0 | 58 | 51 | 51
0 | 0 | 58 | 51 | 51
F =
A =
A =
Median Filter
45 | 52 | 60
45 | 51 | 51
45

## Slide 66
Median Filter
41 | 200 | 60
52 | 45 | 42
0 | 58 | 51
Kiran TALELE
66
F =
To remove noisy pixels, assume virtual rows and columns with repeated border pixel values
41 | 41 | 200 | 60 | 60
41 | 41 | 200 | 60 | 60
52 | 52 | 45 | 42 | 42
0 | 0 | 58 | 51 | 51
0 | 0 | 58 | 51 | 51
F =
A =
A =
Median Filter
45 | 52 | 60
45 | 51 | 51
45
51

## Slide 67
Median Filter
41 | 200 | 60
52 | 45 | 42
0 | 58 | 51
Kiran TALELE
67
F =
To remove noisy pixels, assume virtual rows and columns with repeated border pixel values
41 | 41 | 200 | 60 | 60
41 | 41 | 200 | 60 | 60
52 | 52 | 45 | 42 | 42
0 | 0 | 58 | 51 | 51
0 | 0 | 58 | 51 | 51
F =
A =
A =
Median Filter
45 | 52 | 60
45 | 51 | 51
45
51
51

## Slide 68
Median Filter
41 | 200 | 60
52 | 45 | 42
0 | 58 | 51
Kiran TALELE
68
F =
To remove noisy pixels, assume virtual rows and columns with repeated border pixel values
41 | 41 | 200 | 60 | 60
41 | 41 | 200 | 60 | 60
52 | 52 | 45 | 42 | 42
0 | 0 | 58 | 51 | 51
0 | 0 | 58 | 51 | 51
F =
A =
A =
Median Filter
45 | 52 | 60
45 | 51 | 51
45 | 51 | 51

## Slide 69
Median Filter
41 | 200 | 60
52 | 45 | 42
0 | 58 | 51
Kiran TALELE
69
F =
To remove noisy pixels, assume virtual rows and columns with repeated border pixel values
 | 41 | 200 | 60 | 
 | 52 | 45 | 42 | 
 | 0 | 58 | 51 | 
F =
A =
A =
Median Filter
45 | 52 | 60
45 | 51 | 51
45 | 51 | 51

## Slide 70
Median Filter
41 | 200 | 60
52 | 45 | 42
0 | 58 | 51
Kiran TALELE
70
45 | 52 | 60
45 | 51 | 51
45 | 51 | 51
F =
Input image
with Salt and
Pepper Noise
Median Filtered
output image with eliminated
Salt and Pepper Noise values
A =

## Slide 71
41 | 200 | 60
52 | 45 | 42
0 | 58 | 51
Kiran TALELE
71
F =
45 | 52 | 60
45 | 51 | 51
45 | 51 | 51
A =
Median Filter forces the points with distinct gray levels to be more like their neighbours
When all the pixel values are arranged in order, distinct values occupy extreme positions and Median filter selects median i.e. middle vales of ordered pixel values.
Therefore, noisy pixel values are eliminated median filter

## Slide 72
Kiran TALELE
72
F =
Eliminated noisy pixel values are replaced by one of the neighbouring pixel values.
Therefore, Median Filter is the most suitable to remove Salt and Pepper Noise in the image.
41 | 200 | 60
52 | 45 | 42
0 | 58 | 51
45 | 52 | 60
45 | 51 | 51
45 | 51 | 51
A =

## Slide 73
(i) Max filter is a Non-Linear ordered statistic filter.
(ii) Output pixel value at (x,y) position is obtained by selecting the Maximum of neighbourhood of input pixel value.
(2) Max Filter
Kiran TALELE
73
(i) Min filter is a Non-Linear ordered statistic filter.
(ii) Output pixel value at (x,y) position is obtained by selecting the Minimum of neighbourhood of input pixel value.
(3) Min Filter

## Slide 74
Eg.
Kiran TALELE
74
Max Filter
41 | 200 | 60
52 | 45 | 42
0 | 58 | 51
F =
A =
Min Filter
41 | 200 | 60
52 | 45 | 42
0 | 58 | 51
F =
A =
200
0

## Slide 75
Kiran TALELE
75

## Slide 77
Kiran TALELE
77
Result :

## Slide 78
Sharpening Derivative Filters
Kiran TALELE
78
Sharpening
Filter
Smoothing
Filter
SUM
Integration
Differentiation
Concept :
Difference
Ex. LPF
Ex. HPF

## Slide 79: [ III ] Sharpening First Order Derivative filters [also called as Gradient Filters]
Eg: Robert, Prewit, Sobel and Fri-chen filters
Kiran TALELE
79
Method of differentiation is Gradient
The Gradient of F at (x,y) position is defined as,

## Slide 80
Kiran TALELE
80
Where,

## Slide 81
Kiran TALELE
81
 | f(x-1,y) | 
f(x,y-1) | f(x,y) | f(x,y+1)
 | f(x+1,y) | 
F =
x
y
x+1
x-1
y-1
y+1

## Slide 82
Kiran TALELE
82
F =
Robert Filter
( 1st Order Derivative Sharpening filter )
To find Gx
x
y
-
1
-1
0
0
To find Gy
-1 1
-
0 0

## Slide 83
Kiran TALELE
83
2. Prewit Filter
( 1st Order Derivative - Sharpening filter )
To find Gx
x
y
1 1 1
0 0 0
-1 -1 -1
To find Gy
Gx= (z7–z1)+(z8–z2)+ (z9–z3)
z1 | z2 | z3
z4 | z5 | z6
z7 | z8 | z9
Gx= (z3–z1)+(z6–z4)+ (z9–z7)
-1 0 1
-1 0 1
-1 0 1

## Slide 84
Kiran TALELE
84
To find Gx
x
y
1 2 1
0 0 0
-1 -2 -1
To find Gy
Gx= (z7–z1) +2 (z8–z2) + (z9–z3)
z1 | z2 | z3
z4 | z5 | z6
z7 | z8 | z9
Gy= (z3–z1)+ 2 (z6–z4) + (z9–z7)
-1 0 1
-2 0 2
-1 0 1
3. Sobel Filter
( 1st Order Derivative - Sharpening filter )

## Slide 85
Kiran TALELE
85
To find Gx
x
y
1 1
0 0 0
-1 - - 1
To find Gy
Gx= (z7–z1) + (z8–z2)+(z9–z3)
z1 | z2 | z3
z4 | z5 | z6
z7 | z8 | z9
Gy= (z3–z1)+ (z6–z4)+ (z9–z7)
-1 0 1
- 0
-1 0 1
4. Fri-Chen Filter
( 1st Order Derivative - Sharpening filter )

## Slide 86
Kiran TALELE
86
1. The Magnitude of Gradient at (x,y) is given by,
2. Orientation at (x,y) is given by,
α =

## Slide 87
Kiran TALELE
87
3. To find response of the Gradient filter,
Gradient
Filter
z1 | z2 | z3
z4 | z5 | z6
z7 | z8 | z9
F =
A =
R
where,

## Slide 88
Kiran TALELE
88
Example-1 :
Prewit Gradient
Filter
41 | 200 | 60
52 | 45 | 42
0 | 58 | 51
F =
A =
R
(i) To find Gx
Prewit Vertical Mask is given by,
1 1 1
0 0 0
-1 -1 -1
Gx = (-41) + (-142) + (-9)
Gx = -192

## Slide 89
Kiran TALELE
89
Similarly,
Prewit Gradient
Filter
41 | 200 | 60
52 | 45 | 42
0 | 58 | 51
F =
A =
R
(ii) To find Gy
Prewit Horizontal Mask is given by,
Gy = (19) + (-10) + (51)
Gx = 60
-1 0 1
-1 0 1
-1 0 1

## Slide 90
Kiran TALELE
90
Example...
Prewit Gradient
Filter
41 | 200 | 60
52 | 45 | 42
0 | 58 | 51
F =
A =
R
(iii) To find R
( 192 ) + ( 60 )
( 252 )

## Slide 91: [IV] Second Order Derivative filters Eg. Laplacian Filter, HPF and High Boost Filter
Kiran TALELE
91
The Laplacian of Digital image f at (x,y) position is given by,
(2) Laplacian Filter
The Laplacian filter is Second Order Derivative filter

## Slide 92
Kiran TALELE
92
(i) Find G2x
 | f(x-1,y) | 
f(x,y-1) | f(x,y) | f(x,y+1)
 | f(x+1,y) | 
x
x+1
x-1
y-1 y y+1
Gx = f(x+1,y) - f(x,y)
G2x = [ f(x+1,y) - f(x,y)] – [ f(x,y) - f(x-1,y )]
G2x = f(x+1,y) – 2 f(x,y) + f(x-1,y )
G2x =
0 | 1 | 0
0 | -2 | 0
0 | 1 | 0
G2x =
0 | - 1 | 0
0 | 2 | 0
0 | - 1 | 0
Scale by (-1)

## Slide 93
Kiran TALELE
93
(i) Find G2y
 | f(x-1,y) | 
f(x,y-1) | f(x,y) | f(x,y+1)
 | f(x+1,y) | 
x
x+1
x-1
y-1 y y+1
Gy = f(x, y+1) - f(x,y)
G2y = [ f(x, y+1) - f(x,y)] – [ f(x,y) - f(x, y-1 )]
G2y = f(x, y+1) – 2 f(x,y) + f(x, y-1)
G2y =
0 | 0 | 0
1 | -2 | 1
0 | 0 | 0
G2y =
0 | 0 | 0
-1 | 2 | -1
0 | 0 | 0
Scale by (-1)

## Slide 94
Kiran TALELE
94
(iii) Find
 | f(x-1,y) | 
f(x,y-1) | f(x,y) | f(x,y+1)
 | f(x+1,y) | 
x
x+1
x-1
y-1 y y+1
0 | 0 | 0
-1 | 2 | -1
0 | 0 | 0
0 | 1 | 0
0 | 2 | 0
0 | -1 | 0
+
=
=
0 | -1 | 0
-1 | 4 | -1
0 | -1 | 0
Laplacian 4 directional Mask

## Slide 95
Kiran TALELE
95
(iv) Find
-1 | 0 | -1
0 | 4 | 0
-1 | 0 | -1
0 | -1 | 0
-1 | 4 | -1
0 | -1 | 0
+
=
=
-1 | -1 | -1
-1 | 8 | -1
-1 | -1 | -1
Laplacian 8 directional Mask
=
+
( 4 Directional)
( Diagonal Directional)

## Slide 96
(i) HPF attenuates LOW frequency Components and allows to pass HIGH frequency components of the image.
(2) High Pass Filter
(ii) HPF image can be obtained by subtracting LPF image from the original image.
Kiran TALELE
96
HPF Mask is given by,
-1 | -1 | -1
-1 | 8 | -1
-1 | -1 | -1
w =

## Slide 97
Kiran TALELE
97
Eg. Consider a Digital Image F as given below
0 | 30 | 30 | 0
0 | 30 | 30 | 0
0 | 30 | 30 | 0
10 | 10 | 200 | 200
10 | 10 | 200 | 200
10 | 10 | 200 | 200
100 | 100
100 | 100
100 | 100
10 | 10 | 100 | 100
10 | 10 | 100 | 100
10 | 10 | 100 | 100
10 | 10 | 10 | 100 | 100 | 100
10 | 10 | 10 | 100 | 100 | 100
10 | 10 | 10 | 100 | 100 | 100
10 | 10 | 10 | 100 | 100 | 100
10 | 10 | 10 | 100 | 100 | 100
H P F
 | 0 | 30 | 30 | 0 | 
 | 0 | 30 | 30 | 0 | 
 | 0 | 30 | 30 | 0 | 
-1 | -1 | -1
-1 | 8 | -1
-1 | -1 | -1
W=

## Slide 98
Kiran TALELE
98
NOTE :
Original Image = LPF Image + HPF Image

## Slide 99
Derivation of HPF Mask
L P F
Z1 | Z2 | Z3
Z4 | Z5 | Z6
Z7 | Z8 | Z9
 | A(x,y) | 
Kiran TALELE
99
Consider a Digital Image F and HPF Mask w as shown in figure below,
The response of HPF mask at A(x,y) position is given by,
A(x,y) = z1 w1 + z2 w2 + z3 w3 + … + z9 w9 ……(I)

## Slide 100
Consider a Digital Image F and LPF Mask w as shown in figure below,
L P F
Z1 | Z2 | Z3
Z4 | Z5 | Z6
Z7 | Z8 | Z9
 | B(x,y) | 
The response of LPF mask at B(x,y) position is given by,
Kiran TALELE
100
w =
1 | 1 | 1
1 | 1 | 1
1 | 1 | 1
B(x,y) = z1 z1 + z2 + + … + z9 …… (II)

## Slide 101
Kiran TALELE
101
Now,
Original Image = LPF Image + HPF Image
HPF Image = Original Image - LPF Image
 | A(x,y) | 
=
Z1 | Z2 | Z3
Z4 | Z5 | Z6
Z7 | Z8 | Z9
-
 | B(x,y) | 
At (x,y) position,
A(x,y) = Z5 - B(x,y)

## Slide 102
Kiran TALELE
102
Now, A(x,y) = Z5 - B(x,y)
Where, B(x,y) = z1 z1 + z2 + + … + z9
A(x,y) = Z5 – ( z1 + z2 + + … + z9 )
= Z5 - z1 - z2 - z3 - z4 - z5 … z9 )
A(x,y) = - z1 – z2 - z3 - z4 + z5 …- z9..) ----(III)

## Slide 103
By equating equation (I) and (III) we get,
Kiran TALELE
103
A(x,y) = z1 w1 + z2 w2 + z3 w3 + … + z9 w9 ……(I)
w1= | w2= | w3=
w4= | w5= | w6=
w7= | w8= | W9 =
w =
w =
-1 | -1 | -1
-1 | 8 | -1
-1 | -1 | -1
A(x,y) = - z1 – z2 - z3 - z4 + z5 …- z9..) ----(III)

## Slide 104: High Boost Filter (HBF) Image is obtained by adding HPF image with the original Image.
(3) High Boost Filter
Kiran TALELE
104
HBF Image = Original Image + HPF Image
 | A(x,y) | 
=
Z1 | Z2 | Z3
Z4 | Z5 | Z6
Z7 | Z8 | Z9
+
 | B(x,y) | 
At (x,y) position,
A(x,y) = Z5 + B(x,y)

## Slide 105
Kiran TALELE
105
Now, A(x,y) = Z5 + B(x,y)
= Z5 - z1 - z2 - z3 - z4 + z5 … - z9 )
= - z1 - z2 - z3 - z4 - z5 … - z9 )
Where, B(x,y)
A(x,y) =
By Substituting,
- z1 - z2 - z3 - z4 + z5 … - z9 )
A(x,y) =

## Slide 106
By equating, HBF Mask is then given by,
Kiran TALELE
106
w1= | w2= | w3=
w4= | w5= | w6=
w7= | w8= | W9 =
w =
w =
-1 | -1 | -1
-1 | 17 | -1
-1 | -1 | -1
Let A(x,y) = z1 w1 + z2 w2 + z3 w3 + … + z9 w9
- z1 - z2 - z3 - z4 + z5 … - z9 )
A(x,y) =

## Slide 107: Dr. Kiran TALELE
091-9987030881
kiran.talele@spit.ac.in / ktvtalele@gmail.com
107
107
Academic : PhD
Professional :
  Dean-Students, Alumni & External Relations @ Bharatiya Vidya Bhavans’ Sardar Patel Institute of Technology (SP-IT), Mumbai
  Head-Academic Relation @ Sardar Patel Technology Business Incubator (SP-TBI), Mumbai
  Treasurer-IEEE Bombay Section
https://www.linkedin.com/in/k-t-v-talele/
www.facebook.com/Kiran-Talele-1711929555720263
Stay Connected

## Slide 108
Dr. Kiran TALELE is an Associate Professor in Electronics & Telecommunication Engineering Department of Bharatiya Vidya Bhavans’ Sardar Patel Institute of Technology, Mumbai with 33+ years experience in Academics.
He is a Dean of Students, Alumni and External Relations at Sardar Patel Institute of Technology, Andheri Mumbai.
He is also a Head of Sardar Patel Technology Business Incubator, Mumbai.
His area of research is Digital Signal & Image Processing, Computer Vision, Machine Learning and Multimedia System Design.
He has published 85+ research papers at various national & international refereed conferences and journals. He has filed published 25+ patents at Indian Patent Office. One patent is granted in 2021.
He is a Treasurer of IEEE Bombay Section and Mentor for Startup Incubation & Intellectual Asset Creation.
He is a recipient of P.R. Bapat IEEE Bombay Section Outstanding Volunteer Award 2019.